Presentation title
Master thesis
Magnetic Human Hand Motion Reconstruction
Daniel Müller
Embedded Systems Engineering
22.03.2016

---
„Fix, Schwyz!“ quäkt Jürgen blöd vom Paß.
Systems for Hand Motion Reconstruction
Vision based
High accuracy possible, often used as ground truth
Usually big and static systems
Price and number of cameras rises with demanded accuracy [1, 2]
[Speaker Notes: - Try to get a feeling for the existing approaches - Vison: - Very accurate → Ground truth - Static, big/bulky setup - Glove based: - IMU: many sensors needed, each sensor representes the	orientation of the corresponding bone - Bend sensors - Bridge: another, not yet well explored approach: Magnets!]

---
Systems for Hand Motion Reconstruction
Data gloves
Mobile system
IMUs or bend sensors used
Accuracy is dependent on number of utilized sensor units [3]
Placement of sensors is crucial
Average error to vision based system around 7.1° [4]
[Speaker Notes: - Try to get a feeling for the existing approaches - Vison: - Very accurate → Ground truth - Static, big/bulky setup - Glove based: - IMU: many sensors needed, each sensor representes the	orientation of the corresponding bone - Bend sensors - Bridge: another, not yet well explored approach: Magnets!]

---
Systems for Hand Motion Reconstruction
Magnetic approach
Passive magnetic system using magnets on fingertips [6]
→ Few publications on this
→ Promising approach to build a system which is:
Wearable
Cheap
Easy to use
[Speaker Notes: - Try to get a feeling for the existing approaches - Vison: - Very accurate → Ground truth - Static, big/bulky setup - Glove based: - IMU: many sensors needed, each sensor representes the	orientation of the corresponding bone - Bend sensors - Bridge: another, not yet well explored approach: Magnets!]

---
Passive Magnetic Hand Motion Reconstruction
- Finger postures are determined by joint angles
- Minimizing a nonlinear objective function for estimating K fingers with N magnets
\underset{\mathrm{X}_K}{\text{minimize}} \; \frac{1}{2}|| \tilde{\mathrm{M}} - \mathrm{M}(\mathrm{X}_K) ||^{2}_{2}
With : sensor measurements
        : magnetic flux density for system state
\tilde{\mathrm{M}}
\mathrm{M}(\mathrm{X}_{K})
\mathrm{X}_{K}
[Speaker Notes: Explain approach briefly Magnets on fingertips, sensors on back of hand Picture of my system Try to minimize error between model representation and measurements (Sketch it visualy...) Make statement about system size / state size (dependent on how many measurements/fingers you use) Accompanied challenges (just name them?) Communication OK Sensor calibration OK Earth Cancellation NOT OK]

---
Modeling the Human Hand
Position and orientation of magnet relative to sensor unit is given by the joint angles of the kinematic chain
→ Exact determination of hand dimensions is important!
Anatomics constrain range of motion and set and into relation [7, 8]
→ (single) Finger state vector
→ State vector size for estimating K fingers
\theta_{\mathrm{DIP}}
\theta_{\mathrm{PIP}}
x &= \begin{bmatrix} \theta_{\mathrm{MCP}}\; \theta_{\mathrm{PIP}}\; \phi_{\mathrm{MCP}} \end{bmatrix}^T
size(\mathrm{X}_K) = (3 \times K)
[Speaker Notes: - Make clear, that a finger posture is represented by the 3 angle values]

---
Modeling the static magnets
- Calculation of magnetic flux density by cylindrical model (numerical) [9]
- M is a cumulative sum over the K magnets for each of the N sensors
- Size of M:
- Nonlinearities introduced by position/orientation determination and magnetic models
- To get a fully determined system and unique solutions:
\mathrm{M} &\equiv \begin{bmatrix} {\mathrm{B}}_{1} & {\mathrm{B}}_{2} & \cdots & {\mathrm{B}}_{N} \end{bmatrix}^{T}\\ &= \begin{bmatrix} \sum_{k=1}^{K} \mathrm{B}_1(x_{k})\\[3pt] \sum_{k=1}^{K} \mathrm{B}_2(x_{k})\\ \vdots \\ \sum_{k=1}^{K} \mathrm{B}_N(x_{k})\\ \end{bmatrix} \\ &= \mathrm{M}(\mathrm{X}_K)
size(\mathrm{M}) = (3 \times N)
N \geq K
[Speaker Notes: Mention magnetic foundations briefly From S to N, ... Dipole model assuming bar magnet is a dipole with small distance between S and N shape of magnet in magnetic moment Cylindrical model exact way approximate elliptical integral Transformation between Cartesian and Cyl. coordinates → you can plug in the positions and orientations calculated with hand model for each finger posture]

---
Evaluation of the System
- Comparison to vision based system (Leap Motion)
- Post processing of recorded magnetic data for comparing different minimization formulations
[Speaker Notes: Picture of setup Recording procedure, Leap comparison, offline - estimation]

---
Results
Preliminary – Scaling the measurements
- High difference between model prediction and measurements
  → Induced by hand measured anatomic parameters
- For estimating 1 finger with 1 sensor already 9 values have to be determined
  → Estimation and tuning by trial-and-error not applicable
  → Linear scaling of measurements to model prediction leads to reasonable results
Max deviation unscaled:
Max deviation scaled:
0.018\si{\milli \tesla}
0.005\si{\milli \tesla}
[Speaker Notes: Picture of setup Recording procedure, Leap comparison, offline - estimation]

---
Results
Preliminary – Characteristics of Leap Motion
Minimum
Maximum
Often false interpretation of lateral movement, which did not occur
→ Possibly introduced by direction estimation of Leap
→ Lateral movement of Leap has to be handled with care
\phi_{\mathrm{MCP}} = -0.294\si{\radian}
\phi_{\mathrm{MCP}} = 0.212\si{\radian}
[Speaker Notes: Picture of setup Recording procedure, Leap comparison, offline - estimation]

---
Results
Estimating four fingers
Individual movements not detectable by magnetic system with this configuration due to:
→ False measured hand dimensions
Estimation takes 0.837s per measurement set
→ No real time behaviour
[Speaker Notes: Individual movements not detectable Experiments with perfect data showed, that it should be possible and that the system has to be overdetermined So better results expected by using more sensors]

---
Results
Estimating one finger – best set
Flexion-extension of MCP joint:
→
Adduction-abduction of MCP joint:
→
Bending to fist:
→
→
\mu_{\theta_{\mathrm{MCP}}} = -0.130\si{\radian} \pm 0.003
\mu_{\phi_{\mathrm{MCP}}} = 0.082\si{\radian} \pm 0.0
\mu_{\theta_{\mathrm{MCP}}} = 0.035\si{\radian} \pm 0.004
\mu_{\theta_{\mathrm{PIP}}} = -0.242\si{\radian} \pm 0.062
[Speaker Notes: Plot set 4 (= best set from thesis) Explain all the capabilities and limits of the system Intention of movement is trackable Ad-Ab is trackable Limits due to: Accurance of hand dimensions → Fitting gesture is not perfect but it is a repeatable movement Influence of earth field Acquisition frequency (too low) Also limits of Leap]

---
Results
Estimating one finger – bending to fist
“0-cases” for values occur because no solution is found by the minimizer
This is introduced by:
- Bad accuracy of hand dimensions
- Fitting gesture scales linearly for stretched finger only
\mu_{\theta_{\mathrm{MCP}}} = 0.375\si{\radian} \pm 0.108
\mu_{\theta_{\mathrm{PIP}}} = -0.461\si{\radian} \pm 0.020
\theta_{\mathrm{MCP}}
[Speaker Notes: Plot set 4 (= best set from thesis) Explain all the capabilities and limits of the system Intention of movement is trackable Ad-Ab is trackable Limits due to: Accurance of hand dimensions → Fitting gesture is not perfect but it is a repeatable movement Influence of earth field Acquisition frequency (too low) Also limits of Leap]

---
Results
Estimating one finger – Observations and Limitations
Motion trackable for single flexion-extension of and lateral movement of MCP joint
Results while bending to fist lead to bad values for
Critical influence factors:
  - Accuracy of hand dimensions
    → Can not totally be compensated by fitting gesture
  - Constant position of hand
  - System frequency → Motion speed
Objective function formulation:
  - Cylindrical model
  - System has to be overdetermined
N > K
\theta_ {\mathrm{MCP}}
(= \phi_{\mathrm{MCP}})
\theta_ {\mathrm{MCP}}
[Speaker Notes: Plot set 4 (= best set from thesis) Explain all the capabilities and limits of the system Intention of movement is trackable Ad-Ab is trackable Limits due to: Accurance of hand dimensions → Fitting gesture is not perfect but it is a repeatable movement Influence of earth field Acquisition frequency (too low) Also limits of Leap]

---
Demo

---
Conclusion and Future Work
Reconstruction of a single finger is possible, dependent on several influence factors:
  - Error prone determination of hand dimensions
    → Find a more exact measuring method
  - Influence of earth magnetic field
    → Find a method to cancel the surrounding field dynamically
  - Data acquisition rate of sensor system
  → Employ faster sensors and microcontroller
→ Lowest mean difference to Leap Motion over all 3 finger states for a whole set:
Basic HCI could be one field of application for the presented system
Navigating cursor in two directions
Detecting gestures
27.330\si{\degree} \pm 0.974

---
Bibliography
[1] Northern Digital: Optrak Certus Brochure
[2] Vicon Motion Systems LTD: Vicon Vantage Brochure
[3] Synertial Labs: Synertial, Glove Systems overview
[4] Zecca, Massimiliano et al.: On the development of the bioinstrumentation system WB-1R for the evaluation of human-robot interaction. In: Advanced intelligent mechatronics, 2007 IEEE/ASME
[5] Huang, Jiawei et al.: IM3D: magnetic motion tracking system for dexterous 3D interactions.
      In: ACM SIGGRAPH 2014 Emerging Technologies ACM
[6] Ma, Yanru et al.: Magnetic hand motion tracking system for human-machine interaction.
      In: Electronics letters 46 (2010)
[7] Bullock, Ian M. et al.: Assesing assumptions in kinematic hand models: a review.
      In: Biomedical Robotics and Biomechatronics (BioRob)
[8] Lin, John et al.: Modeling the constraints of human hand motion.
      In: Human Motion, 2000. Proceedings. Workshop on IEEE
[9] Derby, Norman et al.: Cylindrical magnets and ideal solenoids.
      In: Amercan Journal of Physics 78 (2010)

---
Kinematic Hand Model
h_{x} =& \cos(-\theta_{\mathrm{MCP}}-\theta_{\mathrm{PIP}}-\theta_{\mathrm{DIP}})
h_{y} =& \cos(-\theta_{\mathrm{MCP}}-\theta_{\mathrm{PIP}}-\theta_{\mathrm{DIP}})\sin(\phi)
h_{z} =& \sin(-\theta_{\mathrm{MCP}}-\theta_{\mathrm{PIP}}-\theta_{\mathrm{DIP}})\cos(\phi)
l_{Mid} \sin(\frac{\pi}{2}-(\theta_{\mathrm{MCP}}+\theta_{\mathrm{PIP}})) +
l_{Dist}\sin(\frac{\pi}{2}-(\theta_{\mathrm{MCP}}+\theta_{\mathrm{PIP}}+\theta_{\mathrm{DIP}})) + (P_{\mathrm{MCP}_{x}} - P_{Sensor_{x}})
r_{x} = l_{Prox} \sin(\frac{\pi}{2} - \theta_{\mathrm{MCP}}) +
r_{y} = l_{Prox}\cos(\frac{\pi}{2}-\theta_{\mathrm{MCP}}) +
\cdots

---
Cylindircal Magnetic Model
C(k_{c},p,c,s) = \int_{0}^{\frac{\pi}{2}} \frac{c \, \cos^{2}\varphi + s \, \sin^{2}\varphi} {(\cos^{2}\varphi + p \, \sin^{2}\varphi)\sqrt{\cos^{2}\varphi + k_{c}^{2} \, \sin^{2}\varphi}} \; d\varphi

---
Dynamic Cancellation of Earth Magnetic Field
Hold the hand with the sensors attached in a stable and calm position
The magnets for the fingertips are absent
Measure the orientation of the sensors and the corresponding surrounding earth magnetic field
After this calibration phase, track the orientation of the hand
Calculate the relative orientation
Convert into a rotation matrix and apply this to
Subtract the rotated earth magnetic field from your actual measurement:
R_{I}
B_{earth}
R_{h}
R_{d} = R_{I} - R_{h}
R_{d}
rot_{d}
B_{earth}
B = B_{meas} - rot_{d} \cdot B_{earth}